## Slide 1
新操作符
改进的for循环
新的do … while底部检测循环
新的foreach循环
第7章 过程语句
SystemVerilog增加了一些新的操作符和过程语句：更精确的RTL模型、更好地传达设计意图、保证软件工具按同样规则解释语句
新的跳转语句
增强的块命名
语句标号
唯一性与优先级判定

## Slide 2
7.1 新操作符
递增和递减操作符：
++ --
赋值操作符：
+= -= *= /= %= &= |= ^= <<= >>= <<<= >>>=
比较操作符：
==？ !=？
设置成员操作符：
inside
唯一性与优先级操作符:
unique priority
Notes: &= ：位与并赋值；|= ：位或并赋值；^= ：异或并赋值；
<<= ：逻辑左移； <<<= ：算术左移
==? ：通配相等操作符

## Slide 3
7.1.1 递增递减操作符
while (i ++ < LIMIT) begin : loop1
…… //i最后的值为LIMIT
end
while (++ j < LIMIT) begin : loop2
……//j最后的值为LIMIT – 1
end
语句 | 操作 | 描述
j = i ++ | 后加 | i的值赋给j，然后i加1
j = ++ i | 先加 | i加1, 然后i的值赋给j
j = i -- | 后减 | i的值赋给j，然后i减1
j = -- i | 先减 | i减1, 然后i的值赋给j
Notes: 这两个循环区别？
分别循环LIMIT和LIMIT-1次
i, j 最后的值分别为LIMIT + 1和LIMIT（end）之后的值，书上是指循环内的值

## Slide 4
7.1.1递增递减操作符
竞争问题：++ 和 -- 操作符是阻塞赋值，为避免竞争，递增递减操作符只能用于递增递减操作的变量不会被过程块外部语句读取的逻辑建模中！
always_ff @(posedge clock)
if (!resetn) count =0;
else count++;
always_ff @(posedge clock)
case (state)
HOLD: if (count = = MAX)
...
always_ff @(posedge clock)
if (!resetn) count <= 0;
else count <= count + 1;
always_ff @(posedge clock)
case (state)
HOLD: if (count = = MAX)
...
需要非阻塞行为时，避免使用++或- -操作符！！！？？？
Notes: 不是++ 或—操作符问题，而是正确使用信号值问题！
count ++ // same as count = count + 1;
对于左边情况，第二个块可以在++操作之前，也可以在操作之后读取count的值，对于右边情况，由于非阻塞赋值的行为是，所有的并发进程都是先读取变量的值，然后再进行变量的更新赋值，因而可以正确描述时序逻辑间的转换传播。

## Slide 5
7.1.2 赋值操作符
注意：这些赋值操作符是阻塞赋值，同样有竞争问题！！！
操作符 | 功能描述
+= | 等号左边加上等号右边并赋值
-= | 等号左边减去等号右边并赋值
*= | 等号左边乘以等号右边并赋值
/= | 等号左边除以等号右边并赋值
%= | 等号左边除以等号右边，并将得到的余数赋值
&= | 等号左边与等号右边进行位与操作并赋值
¦= | 等号左边与等号右边进行位或操作并赋值
^= | 等号左边与等号右边进行位异或操作并赋值
<<= | 将等号左边逻辑左移右边指定的位数并赋值
>>= | 将等号左边逻辑右移右边指定的位数并赋值
<<<= | 将等号左边算术左移右边指定的位数并赋值
>>>= | 将等号左边算术右移右边指定的位数并赋值
可综合性：
i ++;
if (-- i)
sum = i ++;
可综合性：
b += 5;
b = ( a += 5); //b = a + 5;
Notes: ++, --, +=等操作符，只有单独使用时才是可综合的，如果用于其它的表达式中，则不可综合

## Slide 6
7.1.2 赋值操作符
//example 7-1：
package definitions;
typedef enum logic [2 : 0] {ADD, SUB, MULT, DIV, SL, SR} opcode_t;
typedef enum logic {UNSIGNED, SIGNED} operand_type_t;
typedef union packed {
logic [23 : 0] u_data;
logic signed [23 : 0] s_data;
} data_t;
typedef struct packed {
opcode_t opc;
operand_type_t op_type;
data_t op_a;
data_t op_b;
} instr_t;
endpackage

## Slide 7
7.1.2 赋值操作符
import definitions :: *;
module alu (input instr_t IW,
output data_t alu_out);
always @(IW) begin
if (IW.op_type == SIGNED) begin
alu_out.s_data = IW.op_a.s_data;
unique case (IW.opc)
ADD : alu_out.s_data += IW.op_b.s_data;
SUB : alu_out.s_data -= IW.op_b.s_data;
MULT : alu_out.s_data *= IW.op_b.s_data;
DIV : alu_out.s_data /= IW.op_b.s_data;
SL : alu_out.s_data <<<= 2;
SR : alu_out.s_data >>>= 2;
endcase
end
else ... end endmodule //add the omitted contents
typedef union packed {
logic [23 : 0] u_data;
logic signed [23 : 0] s_data;
} data_t;

## Slide 8
7.1.3 有无关通配符的相等操作符
verilog中有逻辑相等：= =（!=），条件相等：= = =（!= =）
SystemVerilog增加两个操作符：= =?和!=?，在这种操作符中，右操作数中的逻辑位X或Z被看作通配符，它可以与左操作数中相应位的任何值相匹配！
a | b | a= =b | a= = =b | a= =?b | a!=b | a!= =b | a!=?b
0000 | 0000 | 真 | 真 | 真 | 假 | 假 | 假
0000 | 0101 | 假 | 假 | 假 | 真 | 真 | 真
010Z | 0101 | 未知 | 假 | 未知 | 未知 | 真 | 未知
010Z | 010Z | 未知 | 真 | 真 | 未知 | 假 | 假
010X | 010Z | 未知 | 假 | 真 | 未知 | 真 | 假
010X | 010X | 未知 | 真 | 真 | 未知 | 假 | 假
逻辑相等遇到Z或X，结果为未知，条件相等按位对0、1、X、Z进行精确匹配，左右两操作数完全相同，则结果为真，反之为假！
Notes: === 也叫全等操作符
==? 称为通配相等操作符，对两操作数进行按位比较，与==使用类似
作业：把这个表测试一下

## Slide 9
7.1.3 有无关通配符的相等操作符
Verilog中，数字中的逻辑X可以用字符X或x表示，逻辑Z可以用字符z，Z或？表示，如：
logic [7 : 0] opcode;
...
if (opcode = =? 8’b11011???) //屏蔽低三位
如果两个操作数位数不同，通配相等操作符会在比较前将两向量扩展为相同长度，扩展规则与逻辑相等操作符一样。
只有屏蔽位是常数表达式时通配符相等操作符才是可以综合的！！即右操作数不能是变量！
logic [3 : 0] a, b;
logic y1, y2;
assign y1 = (a = = ? 4’b1??1);
assign y2 = (a = =? b); //未试过
Notes: 屏蔽位的位置为固定的表达式

## Slide 10
7.1.4 设置成员操作符—inside
inside是检测一个变量或值是否是某一值集合中一员的操作符。
logic [2 : 0] a;
if (a inside {3’b001, 3’b010, 3’b100})
//if ((a == 3’b001) || (a == 3’b010) || (a == 3’b100))
if (data inside {bus1, bus2, bus3, bus4}) //其它信号集
int d_array [0 : 1023];
if (13 inside d_array) //数组
logic [2 : 0] a;
if (a inside {3’b1?1}) //通配符
//与使用 ==?操作符一样
always_comb begin
case (instruction) inside
4'b0???: opc = instruction[2:0];
4'b1000, 4'b1100: opc = 3'b000;
default: opc = 3'b111;
endcase
end
例子不合适？
Notes: 值集合可以是常数、信号、数组等
inside 与casex的差别？？？
inside可以和if判断和case语句一块使用；
casex将操作符两边的Z和X值都当作无关位，inside只把其后（表达式右边）一系列表达式中的Z和X值当作无关位。

## Slide 11
7.2 操作数改进
Verilog的赋值转换：
reg [63 : 0] a, y, temp;
real r;
temp = r ** 3;
y = a + temp;
类型强制转换：
type’(表达式)
longint a, y;
real r;
y = a + longint’(r ** 3);
尺寸强制转换：
size’(表达式)
logic [15 : 0] a, b, c, sum;
logic carry;
sum = a + 16’(5);
{carry, sum} = 17’(a + 3);
sum = a + 16’(b - 2) / c;
符号强制转换：
signed’(表达式)
unsigned’(表达式)
Notes: sum = signed’(a) + signed’(a); // cast operands
if (unsigned'(a-b) <= 5) // cast intermediate result
verilog类型是自动转换的wire=>reg，real=>reg

## Slide 12
7.3 改进的for循环
Verilog的for循环变量必须在循环体外部声明，SystemVerilog则可以在for语句中直接声明，但该循环变量为局部自动变量，如果要在块外或层次化引用，则必须象Verilog那样在块外说明。
always_ff @(posedge clock) begin
for ( bit [4 : 0] i = 0; i <= 15, i ++)
...
end
for (int i=1, j=0; i*j < 128; i++, j+=3) //Multiple for loop
... // assignments
for (int i = 1, byte j = 0; i * j < 128; i ++, j += 3)
...
Notes: module chip (...); // Verilog style loops
reg [7:0] i;
integer j, k;
always @(posedge clock) begin
for (i = 0; i <= 15; i = i + 1)
for (j = 511; j >= 0; j = j - 1) begin
...
end
end
always @(posedge clock) begin
for (k = 1; k <= 1024; k = k + 2) begin
...
end
end
endmodule

## Slide 13
7.3 改进的for循环
always_comb begin
for (int lo_bit=0; lo_bit<=63; lo_bit++) begin
if (data[lo_bit]) break; // exit loop if
end // bit is set
if (lo_bit > 7) // ERROR: lo_bit is not there
...
end
always_ff @(posedge clock) begin
for (int i = 0; i <= 15; i++) begin
...// i cannot be referenced hierarchically
end
end
Notes: for循环内部声明的变量不能在循环外引用

## Slide 14
7.4 底部检测的do ... while循环
always_comb begin
if (addr < 128 || addr > 255) begin
done = 0;
OutofBound = 1;
outd = mem[128];
end
else while (addr >= 128 && addr <= 255) begin
if (addr = 128) begin
outofBound = 0;
done = 1;
end
else begin
done = 0;
outofBound = 0;
与Verilog相比，SystemVerilog除有while循环外，还有至少执行一次的循环：do ... while，该循环可以简化while循环代码量
end //inner else
outd = mem [addr];
addr - = 1;
end //outer else
end //always
Notes: do <statements>
while (condition);
例题功能：返回地址为128-255中某个存储器的内容，并输出done，outofBound和outd信号。地址为128时done为1，否则为0，未超界时outofBound为0，否则为1。

## Slide 15
7.4 底部检测的do ... while循环
always_comb begin
do begin
done = 0;
OutofBound = 0;
outd = mem[128];
if (addr < 128 || addr > 255)
outofBound = 1;
else if (addr == 128) done = 1;
else outd = mem[addr];
addr - = 1;
end
while( addr >= 128 && addr <= 255);
end ////作业：改成一个能实际运行的模块，并测试之！！
与Verilog相比，SystemVerilog除有while循环外，还有至少执行一次的循环：do ... while，该循环可以简化while循环代码量
Notes: do <statements>
while(condition expresion>;
always_comb begin
do begin
done = 0;
OutofBound = 0;
outd = mem[addr]; //book says this
if (addr < 128 || addr > 255) begin
outofBound = 1;
outd = mem[128]; //book says this
end
else if (addr == 128) done = 1;
addr -= 1;
end while( addr >= 128 && addr <= 255);
end

## Slide 16
always @ * begin //finding the first bit one in a range of bits
begin : loop
integer i;
first_bit = 0;
for (i = 0; i <= 63; i = i + 1) begin : pass
if ( i < start_range) disable pass; //继续循环
if ( i > end_range) disable loop; //跳出循环
if ( data[i]) begin
first_bit = i;
disable loop; //跳出循环
end
end //for
end //loop …
end //always
Verilog采用disalbe实现跳转功能，disable可以跳转到循环结尾继续下一次循环，也可以直接跳出整个循环，难以理解。
7.5 跳转语句
Notes: 查找区间中第一个不等于0的数组元素位置

## Slide 17
//disable在任务所有语句执行完成前提前从任务中返回
task add_up_to_max( input [5 : 0] max, output [63 : 0] result);
integer i
begin
result = 1;
if (max == 0) disable add_up_to_max;
for ( i = 1; i <= 63; i = i + 1) begin
result = result + result;
if (i == max) disable add_up_to_max;
end
end
endtask
7.5 跳转语句
Notes: 返回结果：1<<max

## Slide 18
continue语句：
logic [15 : 0] array [0 : 255];
always_comb begin
for (int i = 0; i <= 255; i ++) begin : loop
if (array [i] == 0) continue; //下一i
transform_function(array[i]);
end //for
end
7.5 跳转语句
break语句：
always_comb begin
first_bit = 0;
for (int i = 0; i <= 63; i ++) begin : loop
if (i < start_range) continue; //下一i
if (i > end_range) break; //跳出循环
if (data [i] ) begin
first_bit = i; break; end //if
end //for
end
SystemVerilog新增了Break, continue, return语句实现跳转

## Slide 19
return语句：
task add_up_to_max (input [5 : 0] max, output [63 : 0] result);
result = 1;
if (max == 0) return; //退出任务
for ( int i = 1; i <= 63; i = i + 1; begin
result = result + result;
if (i == max) return;
end
endtask
7.5 跳转语句
在任务或void函数中，关键字return后面不能有表达式，而在非void函数中return后面一定要有表达式。
disable语句适用所有当前正在执行的任务或块，continue, break, return语句只对当前执行流有效。
Notes: disable不能用于提前从函数中退出
function automatic int log2(input int n);
if ( n <= 1) return 1;
log2 = 0;
while ( n > 1) begin
n = n / 2;
log2 ++;
end
return log2;
endfunction

## Slide 20
always_ff @(posedge clock, posedge reset)
begin
logic breakVar;
if (reset) begin
…
end
else begin
unique case (SquatState)
wait_rx_valid : begin
Rxready <= ‘1;
breakVar = 1;
for (int j = 0; j < NumRx; j += 1) begin : loop1
for (int i = 0; i < NumRx; i += 1) begin : loop2
if Rxvalid[i] && RoundRobin[i] && breakVar) begin
AtMcell <= RxATMcell[i];
Rxready[i] <= 0;
SquatState <= wait_rx_not_valid;
breakVar = 0;
end
end
end
end
…
endcase end end
7.6 改进的块名
Notes: 复杂的设计中总会有很多嵌套的begin … end语句，分辨哪个begin与哪个end匹配不是容易的事情

## Slide 21
always_ff @(posedge clock, posedge reset)
begin : FSM_procedure
logic breakVar;
if (reset) begin : reset_logic
…
end : reset_logic
else begin : FSM_sequencer
unique case (SquatState)
wait_rx_valid : begin :rx_valid_state
Rxready <= ‘1;
breakVar = 1;
for (int j = 0; j < NumRx; j += 1) begin : loop1
for (int i = 0; i < NumRx; i += 1) begin : loop2
if Rxvalid[i] && RoundRobin[i] && breakVar) begin : match
AtMcell <= RxATMcell[i];
Rxready[i] <= 0;
SquatState <= wait_rx_not_valid;
breakVar = 0;
end : match
end : loop2
end : loop1
end : rx_valid_state
…
endcase end : FSM_sequencer end : FSM_procedure
7.6 改进的块名
Notes: SystemVerilog允许在关键词end后面标上与对应begin后面相同的块名，增强代码的可读性
begin : <块名>
…
end : <块名>
end后面的块名是可选的，如果标上的块名与对应begin的块名不同，则系统会报告错误

## Slide 22
always_comb begin : decode_block
decoder : case (opcode)
2’b00 :
outer_loop : for （int i = 0; i <= 15; i ++)
inter_loop : for (int j = 0; j <= 15; j ++)
…
…//对其它操作码值的译码
endcase
end : decode_block
7.7 语句标号
语句标号用于识别单条语句，有助于记录代码及引用这些代码，提高可读性及有助于调试和代码覆盖率分析，带标号的语句可以被disable语句取消。
一个语句块可以有一个块名或标号，但是，不能同时有块名和标号！！！
Notes: 一个begin … end块是一条语句，因此也可以有语句标号，同时它又是块语句，也可以有块名称
begin : block1
…
end : block1
block2_label : begin
…
end

## Slide 23
unique case ( <case_expression>)
…
endcase
priority case ( <case_expression))
…
endcase
7.8 改进的case语句
Verilog标准规定case语句必须按照列举顺序来计算条件选项，这意味着case选项之间存在优先级，如同if … elseif … else中一样。
模拟工具与综合工具对case语句可能有不同的解释：如果所有选项是互斥的，综合工具将会尽量优化掉多余的优先级判定逻辑
Notes: always_comb
case (opcode)
2’b00 : y = a + b;
2’b01 : y = a – b;
2’b10 : y = a * b;
2’b11 : y = a / b;
endcase
end

## Slide 24
always_comb
unique case (opcode)
2’b00 : y = a + b;
2’b01 : y = a – b;
2’b10 : y = a * b;
2’b11 : y = a / b;
endcase
end
7.8.1 unique case条件判断
只有一个条件选项与条件表达式匹配
必须有一个条件选项与条件表达式匹配
不能有重叠的条件
必须指明所有条件
logic [2 : 0] request;
always_comb
casez (request)
3’b1?? : sl1_gnt = 1;
3’b?1? : sl2_gnt = 1;
3’b??1 : sl3_gnt = 1;
endcase
end
logic [2 : 0] opcode;
always_comb
unique case (opcode)
3’b000 : y = a + b;
3’b001 : y = a – b;
3’b010 : y = a * b;
3’b100 : y = a | b;
endcase
end
当opcode为其它值时，将报警！
unique casez (request)
3’b1?? : sl1_gnt = 1;
3’b?1? : sl2_gnt = 1;
3’b??1 : sl3_gnt = 1;
endcase
当表达式值与多个条件选项匹配时，会报警！
每次只发生一个请求，用屏蔽位简化电路
Notes: 任何条件表达式的值都应该与一个且只能与一个条件选项匹配！
unique在模拟时对条件表达式与条件选项进行检查，看看是否满足并行、完全的限制。

## Slide 25
always_comb
priority case (1’b1)
irq0 : irq = 4’b0001;
irq1 : irq = 4’b0010;
irq2 : irq = 4’b0100;
irq3 : irq = 4’b1000;
endcase
end
7.8.2 priority case条件判断
至少有一个条件选项与条件表达式匹配
如果有多个条件选项的值与条件表达式匹配，必须执行第一个匹配分支
必须指明所有条件
当表达式的值无条件选项匹配时，将会报警！避免产生latch。
Priority可以与casex/casez一块使用
Notes: priority表示设计者认为两个或多个条件选项可以同时为真，并且条件选项的顺序非常重要

## Slide 26
unique具有parallel_case和full_case的作用，并检查语法规则；priority具有full_case的作用，并检查语法规则
7.8.3 与full_case和parallel_case区别
always_comb begin
//parallel_case
case(opcode)
2’b00 : y = a + b;
2’b01 : y = a – b;
2’b10 : y = a * b;
2’b11 : y = a / b;
endcase
end
unique和priority保证了软件工具对代码解释的一致性
always_comb begin
//full_case
case(state)
3’b001 : nt_state = 3’b010;
3’b010 : nt_state = 3’b100;
3’b100 : nt_state = 3’b001;
endcase
end
Notes: 使用了parallel_case后，即使有多个条件选项同时满足条件，parallel_case仍然会强制并行求值
unique, priority 与parallel_case, full_case的关系（P158-159）

## Slide 27
logic [2 : 0] sel;
always_comb begin
if (sel == 3’b001) mux_out = a;
else if (sel == 3’b010) mux_out = b;
else if (sel == 3’b100) mux_out = c;
end
7.9 改进的if … else判断语句
Verilog中的if … else … if语句是有优先级顺序的，但这种优先级可能并不是硬件必须的，有可能只是工程师写源代码时任意列出的。

## Slide 28
7.9 unque if … else判断语句
可以并行求值
不能包含重叠的条件
运行期间，对未指明的条件进行警告
logic [2 : 0] sel;
always_comb begin
unique if (sel == 3’b001) mux_out = a;
else if (sel == 3’b010) mux_out = b;
else if (sel == 3’b100) mux_out = c;
end //有未指明条件
logic [2 : 0] sel;
always_comb begin
unique if (sel [0]) mux_out = a;
else if (sel [1]) mux_out = b;
else if (sel [2]) mux_out = c;
end //有重叠项
Notes: 作业：对第一个例子综合一下，看看会不会产生latch!
第二个例子的第1、2、3个判定都有可能为真或同时为真，软件工具会给出不互斥的警告

## Slide 29
7.9 priority if … else判断语句
必须按顺序求值
必须指定所有条件
priority保证了软件工具之间处理的一致性，模拟器、综合器、
等价检查工具和形式验证工具都按同样的方式进行解释。
运行过程中，如果判定序列没有任何分支执行，就会警告，
从而可以检测出是否会产生锁存逻辑！
always_comb begin
priority if (irq0) irq = 4’b0001;
else if (irq1) irq = 4’b0010;
else if (irq2) irq = 4’b0100;
else if (irq3) irq = 4’b1000;
end
Notes: 综合一下该例子

## Slide 30
使用枚举类型建立有限状态机模型
在FSM case语句中使用枚举类型
在FSM case语句中使用always_comb
使用枚举类型和两态类型建模复位逻辑
第8章 有限状态机建模
SystemVerilog可以使用两态类型、枚举类型和用户自定义类型进行高层次抽象建模
应用前面介绍过的always_comb, always_ff, always_latch及枚举类型结合起来，建立有限状态机模型

## Slide 31
module traffic_light (output logic green_light, yellow_light, red_light,
input sensor,
input [15:0] green_downcnt, yellow_downcnt,
input clock, resetN);
enum {RED, GREEN, YELLOW} State, Next; // using enum defaults
always_ff @(posedge clock, negedge resetN)
if (!resetN) State <= RED; // reset to red light
else State <= Next;
8.1使用枚举类型建立状态机模型
介绍使用枚举类型建立有限状态机这样的硬件逻辑需要的规则

## Slide 32
always_comb begin: set_next_state
Next = State; // the default for each branch below
unique case (State)
RED: if (sensor) Next = GREEN;
GREEN: if (green_downcnt == 0) Next = YELLOW;
YELLOW: if (yellow_downcnt == 0) Next = RED;
endcase
end: set_next_state
always_comb begin: set_outputs
{green_light, yellow_light, red_light} = 3'b000;
unique case (State)
RED: red_light = 1'b1;
GREEN: green_light = 1'b1;
YELLOW: yellow_light = 1'b1;
endcase
end: set_outputs
endmodule
8.1使用枚举类型建立状态机模型
典型的三过程建模风格
使用默认的枚举基类int
例子中只有3个状态，int是32位的两态类型
两态类型仿真时的默认初始值会掩盖设计问题
枚举类型默认值可能导致RTL仿真与门级实现不一致？？？
Notes: Int 类型是32位，三个状态最多要3位！
状态没有指定值，综合后可能优化成与RTL不同的值

## Slide 33
module traffic_light (output logic green_light, yellow_light, red_light,
input sensor,
input [15:0] green_downcnt, yellow_downcnt,
input clock, resetN);
enum logic [2 : 0] {RED = 3’b001, // explicit enum definition
GREEN = 3’b010,
YELLOW = 3’b100} State, Next;
always_ff @(posedge clock, negedge resetN)
if (!resetN) State <= RED; // reset to red light
else State <= Next;
8.1.1使用显式枚举类型表示状态编码
利用枚举类型的显式基类型和显式值建模

## Slide 34
always_comb begin: set_next_state
Next = State; // the default for each branch below
unique case (State)
RED: if (sensor) Next = GREEN;
GREEN: if (green_downcnt == 0) Next = YELLOW;
YELLOW: if (yellow_downcnt == 0) Next = RED;
endcase
end: set_next_state
always_comb begin: set_outputs
{green_light, yellow_light, red_light} = 3'b000;
unique case (State)
RED: red_light = 1'b1;
GREEN: green_light = 1'b1;
YELLOW: yellow_light = 1'b1;
endcase
end: set_outputs
endmodule
8.1.1使用显式枚举类型表示状态编码
枚举标签值显式指定
综合编译器将保持显式的枚举标签值，利于综合前后的功能比较
枚举类型的基类型为四态数据类型，需要正确复位
Notes: 四态数据类型初始化值为X，如果不正确复位，RTL模拟将不能进行。

## Slide 35
module traffic_light (output logic green_light, yellow_light, red_light,
input sensor,
input [15:0] green_downcnt, yellow_downcnt,
input clock, resetN);
enum {R_BIT = 0, //状态寄存器中RED状态索引
G_BIT = 1,
Y_BIT = 2} state_bit;
enum logic [2 : 0] {RED = 3’b001 << R_BIT,
GREEN = 3’b001 << G_BIT,
YELLOW = 3’b001 << Y_BIT} State, Next;
always_ff @(posedge clock, negedge resetN)
if (!resetN) State <= RED; // reset to red light
else State <= Next;
8.1.2使用枚举类型的反向case语句
反向case语句：条件表示式和条件选项位置颠倒，对有些综合器，反向case风格的one-hot码状态机会得到更优化的综合结果

## Slide 36
always_comb begin: set_next_state
Next = State; // the default for each branch below
unique case (1’b1) //反向case语句
State[R_BIT] : if (sensor) Next = GREEN;
State[G_BIT] : if (green_downcnt == 0) Next = YELLOW;
State[Y_BIT] : if (yellow_downcnt == 0) Next = RED;
endcase
end: set_next_state
always_comb begin: set_outputs
{green_light, yellow_light, red_light} = 3'b000;
unique case (1’b1) //反向case语句
State[R_BIT] : red_light = 1'b1;
State[G_BIT] : green_light = 1'b1;
State[Y_BIT] : yellow_light = 1'b1;
endcase
end: set_outputs
endmodule
8.1.2使用枚举类型的反向case语句
为什么用两个枚举类型？！！
Notes: 1.上述两种枚举类型，当定义不同的one-hot位时，不会产生编码错误
2.如果设计规范改变了one-hot定义，只需改变指定位置的枚举类型，定义状态名的枚举类型自动反应这一变化。

## Slide 37
unique 指定所有条件选项必须并行求值，而不采用带优先级的编码方式，综合可以优化这些条件选项的译码逻辑
unique case指定条件选项不应该有重叠项，如果条件表达式值满足两个或多个条件选项，仿真时会有警告提示
unique case指定条件选项必须涵盖在仿真中会产生的条件表达式的所有值，如果仿真时，无分支执行，则有警告提示
8.1.3枚举类型与unique case语句
unique case语句减少了case语句的不确定性，在one-hot码状态机中的状态寄存器在某一时刻只有一位是1，也只有一个条件选项与值为1的条件表达式匹配
unique case说明了三件事情：

## Slide 38
// Verilog style case statement with X default
reg ［2 : 0] State, Next; // 3-bit variables
case (State)
3'b001: Next = 3'b010;
3'b010: Next = 3'b100;
3'b100: Next = 3'b001;
default: Next = 3'bXXX;
endcase
8.1.4指定未使用的状态值
case条件表达式中可能有一些未使用的值，进行设计时需要进行相应的处理：赋逻辑值X或使用full_case附注
采用default选项，综合编译器将认为所有在默认条件内的条件表达式值都是未使用值，综合编译器将进一步优化

## Slide 39
// case statement with enumerated X default
enum logic [2:0] {RED = 3'b001,
GREEN = 3'b010,
YELLOW = 3'b100,
BAD_STATE = 3'bxxx
} State, Next;
case (State)
RED: Next = GREEN;
GREEN: Next = YELLOW;
YELLOW: Next = RED;
default: Next = BAD_STATE;
endcase
8.1.4指定未使用的状态值
枚举类型变量不能直接赋X值，如果需要赋X值，枚举类型的基类必须是四态类型，且枚举标签必须用显式X值定义
事实上，SystemVerilog不再需要BAD_STATE枚举值和default条件选项，将枚举类型和unique case结合起来消除了需要使用X赋值以表明存在未使用的条件表达式值情况
Notes: 我的确有一个问题：综合后门级不会出现条件选项以外的情况？No

## Slide 40
enum {R_BIT = 0, // index of RED state in State register
G_BIT = 1, // index of GREEN state in State register
Y_BIT = 2} state_bit;
// shift a 1 to the bit that represents each state
enum logic [2:0] {RED = 3'b001<<R_BIT,
GREEN = 3'b001<<G_BIT,
YELLOW = 3'b001<<Y_BIT} State, Next;
always_comb begin: set_next_state
Next = 3’b000; // clear Next - ERROR: ILLEGAL ASSIGNMENT
unique case (1’b1) // reversed case statement
// WARNING: FOLLOWING ASSIGNMENTS ARE POTENTIAL DESIGN ERRORS
State[R_BIT]: if (sensor == 1) Next[G_BIT] = 1’b1;
State[G_BIT]: if (green_downcnt==0) Next[Y_BIT] = 1’b1;
State[Y_BIT]: if (yellow_downcnt==0) Next[R_BIT] = 1’b1;
endcase
end: set_next_state
8.1.5将状态值赋给枚举类型变量
枚举类型变量只能被赋其类型集合中的值，不能直接对其赋文本值
对枚举类型状态位个别位赋值，可能导致非法值，应尽量避免！！

## Slide 41
enum {WAIT, LOAD, STORE} State, Next;
always @(posedge clock, negedge resetN)
if (!resetN) State <= WAIT;
else State <= Next;
always @(State)
case (State)
WAIT: Next = LOAD;
LOAD: Next = STORE;
STORE: Next = WAIT;
endcase
8.2在FSM中使用两态数据类型
对模型仿真时，在时刻0以前，四态数据类型缺省值是X，而两态类型为0，进行复位时，其操作是将变量清0，因此，当复位逻辑有缺陷时，两态数据类型建模将会掩盖这种缺陷！！
当枚举类型用缺省的基类型时，情况与此相似。
该例子将锁定在状态WAIT，不能正确进行RTL仿真！

## Slide 42
8.2在FSM中使用两态数据类型
解决两态数据类型建模状态锁定办法：
1.采用四态基类型显式声明枚举变量
2.采用always_comb ////？？？
3.将unique case和四态基类型结合使用，可以检测复位是否正确
状态机健壮性（完备状态机）：
应具备初始化状态和默认状态。加电或复位时，进入初始化状态，此外，应有默认（default）状态，这样当状态发生突变时，能保证逻辑不会陷入死循环，即状态具有自恢复功能
Notes: 结合前面的例子说明！！！

## Slide 43
• Module prototypes
• Nested modules
• Simplified netlists of module instances
• Net aliasing
• Passing values through module ports
• Port connections by reference
• Enhanced port declarations
• Parameterized types and polymorphism
• Variable declarations in blocks
Chapter 9 Design Hierarchy
This chapter presents enhancements to Verilog about design hierarchy

## Slide 44
// prototype using Verilog-1995 style
extern module counter (cnt, d, clock, resetN);
// prototype using Verilog-2001 style
extern module counter #(parameter N = 15)
(output logic [N:0] cnt,
input wire [N:0] d,
input wire clock, load, resetN);
9.1 Module prototypes
Module instance in verilog is simple method of creating design hierarchy. but it is difficult to compile a module instance, why?
module and its ports definition is in different place than module instance!
SystemVerilog solves this by module Prototypes:

## Slide 45
9.1 Module prototypes
Extern module declarations can be listed in the same file in which the module is instantiated.
The extern module declaration can be made in any module, at any level of the design hierarchy.
The extern module declaration is only visible within the scope in which it is defined.
It is not necessary for the extern module declaration to be encountered prior to an instance of the module.
Notes: 模块原型本意是解决模块例化时不知道该模块定义的名称、端口等情况，所以在例化前进行说明，但为了与verilog兼容，又可以在其它文件/编译单元域中定义，且可以先例化，再定义原型，这其实背离了引入原型的目的

## Slide 46
9.1.1 Prototype and actual definition
SystemVerilog requires that the port list of an extern module declaration exactly match the actual module definition, including the order of the ports and the port sizes.
To avoid port declaration redundancy, module definition can use .* shortcut.
extern module counter
#(parameter N = 15)
(output logic [N:0] cnt,
input wire [N:0] d,
input wire clock,
input wire load,
input wire resetN);
module counter ( .* );
always @(posedge clock, negedge
resetN) begin
if (!resetN) cnt <= 0;
else if (load) cnt <= d;
else cnt <= cnt + 1;
end
endmodule
Notes: 作业：测试一下模块原型与实例化时端口不一致时，编译器能不能找到错误！！
完全本末倒置了，本来原型是辅助性的，现在却变成了主要的了！！

## Slide 47
9.2 Named ending statements
Named module ends endmodule : <module_name>
The name specified with endmodule must be the same as the name of the module with which it is paired.
Named code block ends
SystemVerilog also allows an ending name to be specified with
other named blocks of code. These include the keyword pairs:
package...endpackage, interface...endinterface,
task...endtask, function...endfunction, and begin...end
Section 7.7 discusses begin … end pairs in more detail.

## Slide 48
9.3 Nested module declarations
In verilog :
module names are global
all module names, user-defined primitive (UDP) names,
and system task and system function names are placed in a global name space.
access to module names is not restricted
it impossible to limit access to specific modules.
global names can cause conflicts
Imagine that both IP models contained the same module name
Two methods: software tools provide proprietary solutions and configuration(verilog 2001)
Modules declared within modules (SystemVerilog)
Notes: 全局模块名产生矛盾的原因：IP来源不同，导致模块名重名

## Slide 49
9.3 Nested module declarations
module chip (input wire clock); // top level of design
dreg i1 (clock);
ip_core i2 (clock);
endmodule: chip
module dreg (input wire clock); // global module definition
...
endmodule: dreg
module ip_core (input wire clock); // global module definition
sub1 u1 (...);
sub2 u2 (...);
module sub1(...); // nested module definition
...
endmodule: sub1
module sub2(...); // nested module definition
...
endmodule: sub2
endmodule: ip_core
Notes: Draw a picture to show the architecture of module chip
It is not common that multiple modules are placed in a file

## Slide 50
9.3 Nested module declarations
module ip_core (input logic clock);
...
`include sub1.v // sub1 is a nested module
`include sub2.v // sub2 is a nested module
...
endmodule
module sub1(...); // stored in file sub1.v
...
endmodule
module sub2(...); // stored in file sub2.v
...
endmodule
Nested module definitions can be in separate files, so that the revision control software can manage the design file easily.
Solution: use `include compiler directive to avoid multiple module in the same file.
Notes: 如果嵌套模块的源代码被掩藏在顶层模块下，代码难以维护、重用困难（需要重用吗？！！！），此外，代码也不简洁！！

## Slide 51
9.3.1 Nested module name visibility
nested module names are not global: the name of a nested module is only visible locally in the parent module, so the nested module can only be instantiated by the parent module, or the hierarchy tree below the parent module.(descendants of the parent)
nested module hierarchy paths: Nested modules have a hierarchical scope name, the same as with any module instance. it can be referenced hierarchally.
nested modules can instantiate other modules: These instantiated modules can be in three name scopes: the global module definition name scope, the parent of the nested module, or within the nested module .
Notes: 名字作用域、层次化引用、可例化的其它模块
第三条画一个简图说明比较清楚

## Slide 52
9.3.2 Instantiating nested modules
nested modules are instantiated the same as regular modules
module ip_core (input clock);
sub1 u1 (...); // instance of nested module sub1
module sub1 (...); // nested module definition
sub2 u2 ();
...
endmodule: sub1
module sub2; // nested module definition
// sub2 does not have ports, but will look in its source
// code parent module (ip_core) for identifiers
sub3 u3 (...);
endmodule: sub2
module sub3 (...); // nested module definition
...
endmodule: sub3
endmodule: ip_core
Notes: The only difference is that nested modules is local, not global.
pls. give the hierarchy diagram of the example.

## Slide 53
nested modules have a local scope : so it’s ports, any nets, variables, tasks, functions or other declarations are only visible in the nested module
The search rules are : name in local nested module, or the parent of the nested module, or the compilation-unit-scope
modules that are not nested search upward in the instantiation tree : names are searched in instantiated module, or compilation-unit-scope
Difference searching rules between nested and non-nested modules: when an identifier is not defined in the nested module, the search path is the parent of the nested module, not instantiation tree
9.3.3 Nested module name search rules
Notes: 嵌套模块内名称作用域，名称搜索规则，非嵌套模块内名称向上搜索与嵌套模块内名称向上搜索区别 P182-183
非嵌套模块内的名称不一定会在例化该模块的层次中搜索：比如如果在一个模块中直接使用一个变量名，该变量则隐含为1bit的logic型变量，而不是去往上搜索！！

## Slide 54
9.4 Simplified netlists of module instances
A netlist is a list of module instances, with nets connecting the ports of the instances together.
two style to connect instances together: ordered port connections and named port connections
ordered port connections: port position is important, but too many ports in a complex design, so it’s prone to make errors.
named port connections: readable, clear, not fallible, and better document, but very verbose
dff d1 (op, /*not used*/, inp, clock, reset); //ordered port connections
dff d1 (.q(op), .qb()/*not used*/, .d(inp), .clk(clock), .rst(reset)); //named port connections
Notes: 网表是用线网将端口连接起来的模块实例的列表
verbose: 冗长，啰嗦

## Slide 55
9.4 Simplified netlists of module instances
module miniPIC ( //MicroChip miniPIC 8-bit processor
inout wire [7:0] port_a_pins,
inout wire [7:0] port_b_pins,
inout wire [7:0] port_c_pins,
input wire clk,
input wire resetN);
wire [11:0] instruct_reg, program_data;
wire [10:0] program_counter, program_address;
wire [ 7:0] tmr0_reg, status_reg, fsr_reg, w_reg, option_reg,
reg_file_out, port_a, port_b, port_c, trisa,
trisb, trisc, data_bus, alu_a, alu_b;
wire [ 6:0] reg_file_addr;
wire [ 3:0] alu_opcode;
wire [ 1:0] alu_a_sel, alu_b_sel;

## Slide 56
9.4 Simplified netlists of module instances
wire reg_file_sel, special_reg_sel, reg_file_enable,
w_reg_enable, zero_enable, carry_enable, skip,
isoption, istris, polarity, carry, zero;
pc_stack pcs ( // module instance with named port connections
.program_counter(program_counter),
.program_address(program_address),
.clk(clk),
.resetN(resetN),
.instruct_reg(instruct_reg),
.data_bus(data_bus),
.status_reg(status_reg));
prom prom1 (
.dout(program_data),
.clk(clk),
.address(program_address));

## Slide 57
9.4 Simplified netlists of module instances
instruction_decode decoder (
.alu_opcode(alu_opcode),
.alu_a_sel(alu_a_sel),
.alu_b_sel(alu_b_sel),
.w_reg_enable(w_reg_enable),
.reg_file_sel(reg_file_sel),
.zero_enable(zero_enable),
.carry_enable(carry_enable),
.polarity(polarity),
.option(isoption),
.tris(istris),
.instruct_reg(instruct_reg));

## Slide 58
9.4 Simplified netlists of module instances
register_files regs (
.dout(reg_file_out),
.tmr0_reg(tmr0_reg),
.status_reg(status_reg),
.fsr_reg(fsr_reg),
.port_a(port_a),
.port_b(port_b),
.port_c(port_c),
.trisa(trisa),
.trisb(trisb),
.trisc(trisc),
.option_reg(option_reg),
.w_reg(w_reg),
.instruct_reg(instruct_reg),

## Slide 59
9.4 Simplified netlists of module instances
.program_data(program_data),
.port_a_pins(port_a_pins),
.data_bus(data_bus),
.address(reg_file_addr),
.clk(clk),
.resetN(resetN),
.skip(skip),
.reg_file_sel(reg_file_sel),
.zero_enable(zero_enable),
.carry_enable(carry_enable),
.w_reg_enable(w_reg_enable),
.reg_file_enable(reg_file_enable),
.zero(zero),
.carry(carry),

## Slide 60
9.4 Simplified netlists of module instances
.special_reg_sel(special_reg_sel),
.isoption(isoption),
.istris(istris)); //register_files
alu alu (
.y(data_bus),
.carry_out(carry),
.zero_out(zero),
.a(alu_a),
.b(alu_b),
.opcode(alu_opcode),
.carry_in(status_reg[0]));

## Slide 61
9.4 Simplified netlists of module instances
glue_logic glue (
.port_b_pins(port_b_pins),
.port_c_pins(port_c_pins),
.alu_a(alu_a),
.alu_b(alu_b),
.expan_out(expan_out),
.expan_addr(expan_addr),
.reg_file_addr(reg_file_addr),
.reg_file_enable(reg_file_enable),
.special_reg_sel(special_reg_sel),
.expan_read(expan_read),
.expan_write(expan_write),
.skip(skip),
.instruct_reg(instruct_reg),
.program_counter(program_counter),

## Slide 62
9.4 Simplified netlists of module instances
.port_a(port_a),
.port_b(port_b),
.port_c(port_c),
.data_bus(data_bus),
.expan_in(expan_in),
.fsr_reg(fsr_reg),
.tmr0_reg(tmr0_reg),
.status_reg(status_reg),
.w_reg(w_reg),
.reg_file_out(reg_file_out),
.alu_a_sel(alu_a_sel),
.alu_b_sel(alu_b_sel),
.reg_file_sel(reg_file_sel),
.polarity(polarity),
.zero(zero));
endmodule

## Slide 63
9.4.1 Implicit .name port connections
.name is an abbreviation of named port connections
.name simplifies connections to module instances
.name infers a connection of a net/variable and port of the same name
.name can be combined with named port connections
.name connection inference rules:
    the net or variable must match both the port name and the port vector size.
      the types on each side of the port must be compatible.
Notes: .name推断规则：1.……；2.……
名字和宽度相同、类型匹配
.name端口映射与顺序无关，如果有未连接，直接空着就行，不需要用逗号隔开

## Slide 64
9.4.1 Implicit .name port connections
module miniPIC ( //MicroChip miniPIC 8-bit processor
inout wire [7:0] port_a_pins,
inout wire [7:0] port_b_pins,
inout wire [7:0] port_c_pins,
input wire clk,
input wire resetN);
wire [11:0] instruct_reg, program_data;
wire [10:0] program_counter, program_address;
wire [ 7:0] tmr0_reg, status_reg, fsr_reg, w_reg, option_reg,
reg_file_out, port_a, port_b, port_c, trisa,
trisb, trisc, data_bus, alu_a, alu_b;
wire [ 6:0] reg_file_addr;
wire [ 3:0] alu_opcode;
wire [ 1:0] alu_a_sel, alu_b_sel;

## Slide 65
9.4.1 Implicit .name port connections
wire reg_file_sel, special_reg_sel, reg_file_enable,
w_reg_enable, zero_enable, carry_enable, skip,
isoption, istris, polarity, carry, zero;
pc_stack pcs ( // module instance with named port connections
.program_counter,
.program_address,
.clk,
.resetN,
.instruct_reg,
.data_bus,
.status_reg);
prom prom1 (
.dout(program_data),
.clk,
.address(program_address));

## Slide 66
9.4.1 Implicit .name port connections
instruction_decode decoder (
.alu_opcode,
.alu_a_sel,
.alu_b_sel,
.w_reg_enable,
.reg_file_sel,
.zero_enable,
.carry_enable,
.polarity,
.option(isoption),
.tris,
.instruct_reg);

## Slide 67
9.4.1 Implicit .name port connections
register_files regs (
.dout(reg_file_out),
.tmr0_reg,
.status_reg,
.fsr_reg,
.port_a,
.port_b,
.port_c,
.trisa,
.trisb,
.trisc,
.option_reg,
.w_reg,
.instruct_reg,

## Slide 68
9.4.1 Implicit .name port connections
.program_data,
.port_a_pins,
.data_bus,
.address(reg_file_addr),
.clk,
.resetN,
.skip,
.reg_file_sel,
.zero_enable,
.carry_enable,
.w_reg_enable,
.reg_file_enable,
.zero,
.carry,

## Slide 69
9.4.1 Implicit .name port connections
.special_reg_sel,
.isoption,
.istris); //register_files
alu alu (
.y(data_bus),
.carry_out(carry),
.zero_out(zero),
.a(alu_a),
.b(alu_b),
.opcode(alu_opcode),
.carry_in(status_reg[0]));

## Slide 70
9.4.1 Implicit .name port connections
glue_logic glue (
.port_b_pins,
.port_c_pins,
.alu_a,
.alu_b,
.expan_out,
.expan_addr,
.reg_file_addr,
.reg_file_enable,
.special_reg_sel,
.expan_read,
.expan_write,
.skip,
.instruct_reg,
.program_counter,

## Slide 71
9.4.1 Implicit .name port connections
.port_a,
.port_b,
.port_c,
.data_bus,
.expan_in,
.fsr_reg,
.tmr0_reg,
.status_reg,
.w_reg,
.reg_file_out,
.alu_a_sel,
.alu_b_sel,
.reg_file_sel,
.polarity,
.zero);
endmodule

## Slide 72
9.4.2 Implicit .* port connections
The .* syntax indicates that all ports and nets (or variables) of the same name should automatically be connected together for that module instance.
As with the .name syntax, for a connection to be inferred, the name and vector size must match exactly, and the types connected together must be compatible.
Notes: 隐式的.*端口连接
名字、宽度、类型

## Slide 73
9.4.2 Implicit .* port connections
module miniPIC ( //MicroChip miniPIC 8-bit processor
inout wire [7:0] port_a_pins,
inout wire [7:0] port_b_pins,
inout wire [7:0] port_c_pins,
input wire clk,
input wire resetN);
wire [11:0] instruct_reg, program_data;
wire [10:0] program_counter, program_address;
wire [ 7:0] tmr0_reg, status_reg, fsr_reg, w_reg, option_reg,
reg_file_out, port_a, port_b, port_c, trisa,
trisb, trisc, data_bus, alu_a, alu_b;
wire [ 6:0] reg_file_addr;
wire [ 3:0] alu_opcode;
wire [ 1:0] alu_a_sel, alu_b_sel;

## Slide 74
9.4.2 Implicit .* port connections
wire reg_file_sel, special_reg_sel, reg_file_enable,
w_reg_enable, zero_enable, carry_enable, skip,
isoption, istris, polarity, carry, zero;
pc_stack pcs ( // module instance with named port connections
.*);
prom prom1 (
. *,
. dout(program_data),
.address(program_address));
instruction_decode decoder (
.*,
.option(isoption));

## Slide 75
9.4.2 Implicit .* port connections
register_files regs (
.*,
.dout(reg_file_out),
.address(reg_file_addr));
alu alu (
.y(data_bus),
.carry_out(carry),
.zero_out(zero),
.a(alu_a),
.b(alu_b),
.opcode(alu_opcode),
.carry_in(status_reg[0]));
glue_logic glue (
.*);
endmodule

## Slide 76
9.5 Net aliasing
SystemVerilog adds an alias statement to create two or more names for the same net.
alias is not the same as copy
alias is not the same assign(assign statement copy the rignt-hand value to the left-hand variable)
changes on any aliased net affect all aliased nets
aliases are not order dependent
wire reset, rst, resetN, rstN;
alias rst = reset;
alias reset = resetN;
alias resetN = rstN; // alias rst = resetN = rstN = reset;

## Slide 77
9.5.1 alias rules
SystemVerilog imposes several restrictions on what signals can be aliased to another name.
only net types can be aliased
only nets of the same type can be aliased(wire VS wire, wand VS wand, etc.)
only nets of the same size can be aliased
wire [31:0] n1;
wire [3:0][7:0] n2;
alias n2 = n1;
wire [39:0] d_in;
wire [7:0] crc;
wire [31:0] data;
alias data = d_in[31:0]; // 32 bit nets
alias crc = d_in[39:32]; // 8 bit nets
Notes: Variables cannot be aliased.
线网的一位/部分位也可以进行别名化

## Slide 78
9.5.2 Implicit net declarations
implicit net can be inferred from an alias, it is not necessary to first explicitly declare each of the nets in the alias.
An undeclared identifier name on either side of an alias statement will infer a net type.
The default implicit net type is wire. This can be changed with the ‘default_nettype compiler directive.
If the net name is listed as a port of the containing module, the implicit net will be the same vector size as the port.
If the net name is not listed in the containing module’s port list, then a 1-bit net is inferred.
Net aliasing can also be used to define a net that represents part of another net.

## Slide 79
9.5.2 Implicit net declarations
module register (output [63:0] q,
input [63:0] d,
input clock, reset);
//wire [63:0] outp, inp;
alias inp = d; // infers inp is a 64-bit wire
alias outp = q; // infers outp is a 64-bit wire
alias rstN = reset; // infers 1-bit wires
wire [63:0] data;
wire [7:0] lo_byte, hi_byte;
alias data[7:0] = lo_byte;
alias hi_byte = data[63:56];
alias tmp = data[31:0]; //ok?
endmodule
在output 后面加上logic看看什么结果
增加一个always块，在块中给q赋一个值，比较有无logic的结果
测试tmp为多少位？
Notes: systemVerilog中模块的输出在未给出数据类型声明的情况下，缺省为线网类型，它不能在过程块中被赋值！与verilog规则一致
Inp, outp被推断为64位wire类型

## Slide 80
9.5.3 Using aliases with .name and .*

## Slide 81
9.5.3 Using aliases with .name and .*
module chip (input wire master_clock,
input wire master_reset,
...);
wire [31:0] address, new_address, next_address;
ROM i1 ( .*, // infers .address(address)
.data(new_address),
.clk(master_clock) );
program_count i2 ( .*, // infers .next_address(next_address)
.jump_address(new_address),
.clock(master_clock),
.reset_n(master_reset) );

## Slide 82
9.5.3 Using aliases with .name and .*
address_reg i3 ( .*, // no connections can be inferred
.next_addr(next_address),
.current_addr(address),
.clk(master_clock),
.rstN(master_reset) );
endmodule
module ROM (output wire [31:0] data,
input wire [31:0] address,
input wire clk);
...
endmodule

## Slide 83
9.5.3 Using aliases with .name and .*
module program_count (output logic [31:0] next_address,
input wire [31:0] jump_address,
input wire clock, reset_n);
...
endmodule
module address_reg (output wire [31:0] current_addr,
input wire [31:0] next_addr,
input wire clk, rstN);
...
endmodule

## Slide 84
9.5.3 Using aliases with .name and .*
module chip (input wire master_clock,
input wire master_reset,
...);
wire [31:0] address, data, new_address, jump_address,
wire [31:0] next_address, next_addr, current_addr;
alias clk = clock = master_clock;
alias rstN = reset_n = master_reset;
alias data = new_address = jump_address;
alias next_address = next_addr;
alias current_addr = address;
ROM i1 ( .* );
program_count i2 ( .* );
address_reg i3 ( .* );
endmodule // using aliases can simplify netlists

## Slide 85
9.9 Parameterized types
Modules that can be redefined using parameters are often referred to as parameterized modules.
verilog can use parameter or localparam constants to calculate the vector widths of module ports or other declarations.
SystemVerilog adds a significant extension to the concept of redefinable, parameterized modules.
The net and variable types of a module can be parameterized in SystemVerilog.
Parameterized types are synthesizable, provided the default or redefined types are synthesizable types.
Notes: Sections 9.6-9.8 can be referred chapter5 and chapter6
可以重新定义参数的模块称为参数化模块

## Slide 86
9.9 Parameterized types
module adder #(parameter type ADDERTYPE = shortint)
(input ADDERTYPE a, b, // redefinable type
output ADDERTYPE sum, // redefinable type
output logic carry);
ADDERTYPE temp; // local variable with redefinable type
... // adder functionality
endmodule
module big_chip( ... );
shortint a, b, r1;
int c, d, r2;
int unsigned e, f, r3;
wire carry1, carry2, carry3;
adder i1 (a, b, r1, carry1); // 16-bit signed adder
adder #(.ADDERTYPE(int)) i2 (c, d, r2, carry2); // 32-bit signed adder
adder #(.ADDERTYPE(int unsigned)) i3 (e, f, r3, carry3); // 32-bit unsigned adder
endmodule